## Slide 1
GROUP CODE · SURGE 090
Progress Review (Design & Development)
Smart Snake Robot
with Dynamixel Smart Servo Motors
Shashank Jangir
ENTRY NO.
2024EE11048
Bhavesh Bansiwal
ENTRY NO.
2024ME10487
Mahima Chotiya
ENTRY NO.
2024ME11187
INSTITUTION
Indian Institute of Technology, Delhi
PROJECT GUIDE
Professor Amartansh Dubey
PROJECT REPOSITORY
https://github.com/shashankjangir/SurGe-090-Smart-snake-robot
Notes: Title slide for the 25% progress review of the Smart Snake Robot project, Group SURGE 090. Introduce the team and milestone scope.

## Slide 2
ACTUATOR SELECTION STUDY
Why Dynamixel Motors?
THE REQUIREMENT
A snake robot drives many joints at once. The actuator must deliver:
Precise position control
Simple wiring architecture
Scalability for multiple joints
Reliable communication
Real-time feedback
Compact size & sufficient torque
OPTIONS COMPARED
Criterion | Conventional Servo | Dynamixel Smart Servo
Communication | Individual signal wire per motor | Daisy-chain communication
Wiring Complexity | High | Low
Feedback | Not available | Position, load, temperature, voltage feedback
Controller | External controller required | Built-in controller
Scalability | Difficult for many joints | Designed for multi-joint robots
Precision | Moderate | High
Robotics Applications | Hobby projects | Research and industrial robotics

## Slide 3
ARCHITECTURE & DECISION
Daisy-Chain Architecture & Final Selection
Conventional Servo — Separate Wiring
Controller
Servo 1
Servo 2
Servo 3
Servo 4
Every motor needs its own signal wire back to the controller.
Dynamixel — Daisy-Chain
Ctrl
M1
M2
M3
M4
One cable carries power and data to every joint in sequence.
KEY LEARNINGS
Daisy-chain wiring sharply cuts cabling and assembly effort.
A controller built into every motor simplifies integration.
Real-time feedback enables future closed-loop control.
Compact form factor suits modular robot segments.
High precision and smart control fit advanced robotics.
FINAL SELECTED ACTUATOR
Dynamixel XL330 Series
Chosen for its smart serial communication, full-state feedback, compact form factor and effortless multi-joint scaling — the right fit for a multi-segment snake robot.

## Slide 4
GOALS & EXPECTED OUTCOMES
What This Project Sets Out to Build
01
Modular Architecture
A repeatable segment-based mechanical design.
02
Dynamixel Actuators
Integrate smart servos with daisy-chained control.
03
Raspberry Pi Control
A single-board-computer control system.
04
Locomotion Algorithms
Implement serpentine and gait-based motion.
05
Sensor Integration
Add sensing for future intelligent navigation.
06
Scalable Platform
Keep it maintainable and easy to extend.
Notes: Six concrete goals across mechanics, actuation, computing, control, sensing and scalability. These map to the timeline phases.

## Slide 5
WORK COMPLETED SO FAR
Quarter-One Progress Summary
OVERALL COMPLETION(till now)
25 %
Phase 1 complete · Phase 2 underway
10
Tasks done
2
Segments printed
1
Pi configured
COMPLETED TASKS
Literature review & project understanding
Hardware selection & BOM preparation
CAD design of snake-robot segment
Assembly sized to Dynamixel XL330 dims
3D printing of two prototype segments
Raspberry Pi setup & configuration
Wi-Fi connectivity testing on the Pi
Basic Raspberry Pi lab projects executed
GitHub repository created & maintained
Procurement process initiated
Notes: About a quarter done: ten tasks closed across research, mechanical design, fabrication and the compute platform.

## Slide 6
Power Supply
Raspberry Pi 5 [Central Controller]
Communication Layer (U2D2 / UART)
Dynamixel Motor Network
Robot Segments (10 × servo joints)
Control Algorithms
IMU / Force Sensors
Camera Module
Wireless Control Module
LEGEND
Implemented
In Progress
Planned Future Work
Current Implementation Status
Raspberry Pi 5 configured and tested
Communication architecture defined
Mechanical segments fabricated
Dynamixel integration pending hardware
SYSTEM ARCHITECTURE
Conceptual Block Diagram
Architecture finalized · Implementation in progress
FUTURE INTEGRATION
Notes: Controller at the centre. Solid cyan = implemented/in progress; dashed amber (sensors, camera) = designed-in but scheduled for a later phase.

## Slide 7
CAD DESIGN DEVELOPMENT
A Segment Designed Around the Motor
The CAD model is built to the exact dimensions of the Dynamixel XL330-M288 servo, using a modular, segment-based architecture focused on manufacturability and scalability.
DESIGN CONSIDERATIONS
Motor mounting — Precise seats for XL330 servo bodies.
Structural rigidity — Stiff frame to resist motion loads.
Cable routing — Clean daisy-chain channels for wiring.
Electronics ready — Space reserved for future boards.
ASSEMBLY FLOW
Motor → Segment Parts → Full Chain Assembly
① Motor
② Segment Parts
③ Full Assembly
③ Full Assembly
Notes: CAD modelled to real XL330 dimensions so printed parts mate with the actual servos. Replace the placeholder with CAD screenshots.

## Slide 8
PROTOTYPE FABRICATION
From Model to Printed Hardware
PRINTED SEGMENT — PHOTO 1
Insert photo of the first 3D-printed segment
PRINTED SEGMENT — PHOTO 2
Insert photo of the second segment / assembly
FABRICATION STATUS
Two prototype segments 3D printed
Both segments produced from the CAD model.
DONE
Initial dimensional verification done
Printed parts measured against design specs.
DONE
Physical validation of CAD initiated
Checking fit, tolerances and assembly.
NEXT
Preparing for motor-integration tests
Next: seat XL330 servos into segments.
NEXT
Notes: Two segments printed and measured, validating the CAD. Next step is servo integration. Drop prototype photos on the left.

## Slide 9
Raspberry Pi 5 received & configured
Raspberry Pi OS installation completed
Wi-Fi connectivity established
SSH & remote access explored
Basic GPIO & intro projects performed
Linux environment & Python familiarity
Raspberry Pi Platform Successfully Configured and Tested
Raspberry Pi OS Desktop
GPIO / Python Testing
SSH Remote Access
System Configuration
Development Environment Setup
PROGRESS MILESTONES
Standing Up the Compute Platform
RASPBERRY PI LEARNING & DEVELOPMENT
Notes: Control computer is live: OS installed, networked, remotely accessible, exercised with intro GPIO and Python. De-risks software before motors arrive.

## Slide 10
HARDWARE PROCUREMENT & RESOURCE AVAILABILITY
Hardware Procurement & Resource Availability
Hardware Strategy: Raspberry Pi 4 was planned in the BOM; however, a Raspberry Pi 5 was already available in the laboratory, enabling immediate software development and testing without waiting for delivery. To accelerate development, the team utilised the laboratory Raspberry Pi 5 platform while the ordered components remain under procurement.
AVAILABLE & IN USE
ORDERED — AWAITING DELIVERY
COMPLETED PREPARATORY WORK
Raspberry Pi 5 (Laboratory Resource)
Raspberry Pi Starter Kit
Raspberry Pi OS Environment
GitHub Repository
3D Printed Prototype Segments
Dynamixel XL330 Smart Servo Motors
U2D2 Communication Interface
U2D2 Power Hub Board
Dynamixel Communication Cables
5V Power Supply
ESP32 Development Board
Hardware selection finalised
Bill of Materials prepared
CAD model completed
Segment fabrication initiated
Software environment configured
DEVELOPMENT PROGRESS
✓
Component
Selection
✓
Procurement
Initiated
✓
CAD
Design
✓
Prototype
Printing
✓
RPi
Learning
⏳
Motor
Integration
Awaiting HW
→
Locomotion
Testing
Upcoming
★
Key Achievement: Although the primary Dynamixel hardware has not yet arrived, the team has successfully utilised available laboratory resources to complete design, fabrication, documentation, and software preparation activities, ensuring project progress is maintained.
Notes: Live BOM from the purchasing sheet. Compute hardware in hand; actuation and power chain ordered. Total approx Rs 33,760.

## Slide 11
REPOSITORY & DOCUMENTATION
Version Control From Day One
1
Repository created
Central home for the whole project.
2
Version control established
Tracked, reversible change history.
3
CAD files uploaded
Design source committed to the repo.
4
Design iterations documented
Every revision captured in commits.
5
Progress tracking in place
Milestones and issues logged.
6
Team collaboration workflow
Shared branches and pull requests.
GitHub repository — project root & structure
Commit history — tracked iterations & uploads
GITHUB REPOSITORY SCREENSHOTS
✓ All milestones tracked in GitHub
Notes: The repo is the single source of truth — CAD, docs, tracked iterations — with a collaboration workflow already running.

## Slide 12
PROJECT TIMELINE
Eight Phases · Currently at 25%
PHASE 1
Research & Design
Completed
1
PHASE 2
Hardware Procurement
In progress
2
PHASE 3
Mechanical Assembly
Up next
3
PHASE 4
Motor Integration
4
PHASE 5
Control Algorithms
5
PHASE 6
Sensor Integration
6
PHASE 7
Testing & Optimisation
7
PHASE 8
Final Demonstration
8
WE ARE HERE
Notes: Eight-phase plan: Phase 1 complete, Phase 2 active, Phase 3 next — about 25%. Phases 4-8 cover integration, control, sensing, testing, demo.

## Slide 13
CURRENT ACHIEVEMENTS
Concrete Wins in Quarter One
Architecture finalized
System block diagram locked.
CAD design completed
Segment modelled to motor specs.
Prototype fabrication started
Two segments printed & checked.
Pi environment established
OS, network and tooling ready.
GitHub workflow operational
Version control and docs live.
Procurement initiated
Core compute received; rest ordered.
Notes: Six headline achievements: design, fabrication, compute, tooling and procurement all moving — a working foundation.

## Slide 14
SIMULATION & VALIDATION
Simulation-Based Validation of Control Architecture
Wokwi-based simulation environment developed to validate locomotion control, sensor integration, and communication architecture before physical Dynamixel hardware arrival.
SIMULATION OBJECTIVE
A virtual testing platform to validate the control architecture before Dynamixel actuators and communication hardware arrive — enabling software development, algorithm verification, and sensor integration in parallel with procurement.
COMPONENTS SIMULATED
Controller
Sensors
Display
Actuators
ESP32 · 5-Servo joint network · MPU6050 IMU · HC-SR04 ultrasonic · SSD1306 OLED · control & communication framework
FUNCTIONAL VALIDATION COMPLETED
ENGINEERING BENEFITS
Multi-joint servo coordination
Travelling-wave serpentine gait generation
Obstacle detection via ultrasonic sensing
IMU integration for orientation feedback
OLED-based system status monitoring
Sensor–controller–actuator communication
Reduced dependence on hardware delivery timelines
Enabled early software debugging & control-architecture verification
Established migration path to Raspberry Pi 5 + Dynamixel XL330, reducing integration risk
KEY OUTCOME A complete software-validation framework was developed, allowing locomotion, sensing, and control workflows to be tested before physical robot assembly.

## Slide 15
FUTURE WORK & DEVELOPMENT ROADMAP
Planned Activities for the Next Development Phase
1
Hardware Arrival
Receive Dynamixel XL330 motors
Receive U2D2 interface
Verify purchased components
2
Mechanical Assembly
Assemble complete snake body
Install Dynamixel actuators
Route communication cables
3
Communication Setup
Configure motor IDs
Establish serial communication
Validate daisy-chain architecture
4
Locomotion Development
Port simulation code to Pi 5
Implement serpentine locomotion
Synchronize multi-joint movement
5
Sensor Integration
Integrate MPU6050 IMU
Integrate obstacle detection
Implement feedback control
6
Testing & Optimization
Motion performance testing
Power & reliability analysis
System optimization
Completed phase
Ongoing work
Future milestone
EXPECTED DELIVERABLES
Fully assembled snake robot
Dynamixel-based locomotion
Sensor-assisted navigation
Integrated Raspberry Pi 5 control system
Demonstration-ready prototype
Final SURGE project showcase
TARGET FOR NEXT REVIEW
Complete hardware integration
Demonstrate basic snake locomotion
Validate communication architecture
Validate sensing framework
Goal: ~60–70% project completion

## Slide 16
WHAT CHANGED SINCE THIS REVIEW
Generation 2 — Corrections & Cause
This slide records what has since been superseded.
Constraint
WHAT HAPPENED
2 of 10 XL330 received, then the part vanished
Six-week stall
IMPACT
Control stack written against absent hardware
Re-architecture
COMMIT a32b675 · 2026-08-20
“No dynamixel in the market. So switched to Servos”
 | THAT DECK SAID | TODAY | WHY
 | XL330 · U2D2 · Power Hub — “ORDERED, AWAITING DELIVERY” | Order cancelled. 10× ST3215 + Waveshare ESP32 driver in hand | Part unobtainable in India
 | “Eight Phases · Currently at 25%” | Phase 3 — Fabrication & Assembly | Eight weeks of Gen 2 work since
 | “Prototype fabrication started” | Gen 1 segments printed; Gen 2 v6 printed | Design of record changed
 | Roadmap step 1 — “Receive Dynamixel XL330 motors” | Superseded — see slide 29 | Different motors received
WHAT IT BOUGHT 5.7× joint torque (0.52 → 2.94 N·m) · a 12 V rail · sourceable in India — consequences of the switch, not its reason. Torque budget: slide 23.
Notes: Open by saying the deck up to this point is unchanged from the 25 percent review and is being left that way deliberately - those slides are a record of what we believed then, not a claim about now. Then walk the register top to bottom. It takes about forty seconds and it pre-empts every 'but slide 10 says' interruption in the second half. Say the honest version of the pivot out loud: this was a procurement failure, not an engineering preference, and a re-architecture under a supply constraint is a legitimate result. The follow-up question a reviewer asks is 'where is your torque budget' - it is slide 23, and it did not exist at the 25 percent review.

## Slide 17
CURRENT UPDATE
The planar robot is working; Gen 3 is next
GEN 2.0
Working planar robot
Onboard and bench control are operating.
GEN 2.1
Shared host control
Dashboard and gamepad support tuning and steering.
GEN 3.0
In development
Alternating yaw and pitch joints extend the mechanism.
Current Gen 2 prototype photo
Place: gen2-st3215/media/20260925_164442.jpg
SURGE-090 • Current development update

## Slide 18
DESIGN DECISION
The actuator changed; the modular idea stayed
GEN 1 REFERENCE
Original Dynamixel design
ARCHITECTURE
Ten coordinated joints
INTERFACE
Dynamixel communication
POWER
Original distribution concept
→
GEN 2 IMPLEMENTATION
ST3215 platform
ARCHITECTURE
Ten-joint modular idea retained
INTERFACE
Communication moved to the ST3215 bus
MECHANICS + POWER
Mounts, wiring and distribution redesigned together
ST3215 reference photo
waveshare servo photo.png
The actuator decision changed mechanics, wiring and software together.

## Slide 19
PHYSICAL ASSEMBLY
Eleven segments, ten coordinated joints
WORKING CHAIN
Modular body sections
Ten yaw joints
Daisy-chained servo connections
Full-chain assembly photo
Place: gen2-st3215/media/20260923_224427.jpg
Preserve the complete visible chain.
Joint numbers indicate order, not measured timing.

## Slide 20
MECHANICS + CONTACT
Ground contact is part of the mechanism
PHYSICAL EVIDENCE NEEDED
Joint / belly close-up
Add a physical photo showing the yoke, motor retention and contact surface.
V6 DESIGN
Matching CAD view
Add the v6 geometry without implying the current build uses that revision.
Yokes carry load
→
Retention holds motor
→
Belly features resist lateral slip
Design principle only; traction, clearance and directional friction still require measurement.

## Slide 21
POWER DESIGN V3
Power reaches the servos in five pairs
3S LiPo
Main fuse
+ disconnect
Five fused pairs
Servos 1–2
Servos 3–4
Servos 5–6
Servos 7–8
Servos 9–10
Buck supply
Controller
DATA / GND
Servo power
DATA / GND
Installed wiring photo
Optional evidence inset
Distribution concept shown; installed fuse ratings and runtime require current hardware inspection.

## Slide 22
GEN 2.0 • ONBOARD ARRANGEMENT
Gen 2.0 keeps the gait on the robot
Robot ESP32
robot_esp32_v2 computes gait
targets
Servo chain
current feedback returns locally
telemetry
Base ESP32
ESP-NOW link
Base ESP32
telemetry receiver
Raspberry Pi
display / logging
Reverse
→
Turn
→
Resume
Thresholds and evasion reliability remain calibration topics; obstacle side is not inferred.

## Slide 23
GEN 2.1 • HOST ARRANGEMENT
Gen 2.1 moves target generation to the host
PC / Pi app
Shared gait controller
→
USB or transmitter
Command relay
→
Receiver
Applies targets
→
Servo bus
Targets + feedback
COMMAND DIRECTION →
Sensor node
Separate input path
← FEEDBACK DIRECTION
The receiver returns servo feedback to the host-side application.
MOTION-STATE GUARD
Start, stop and a 750 ms target timeout manage command state.
Gen 2.1 does not inherit the Gen 2.0 battery/temperature cutoffs or evasion state machine.

## Slide 24
GAIT CONTROLLER
A travelling wave coordinates the joints
θᵢ(t) = A sin(ωt − iφ) + b
A = amplitude • ω = temporal frequency
φ = phase lag • b = steering bias
PHASE 1
PHASE 2
PHASE 3
Physical counterpart
Place: 20260925_164828.jpg
Controller illustration; not a measured trajectory.
TEN JOINTS • THREE STATES

## Slide 25
SHARED SOFTWARE
One controller, several ways to work with it
Gen 2.1 dashboard screenshot
Reserve a current, clearly identified SIM or hardware-state view.
11-link PyBullet view
Optional secondary image
Dashboard for tuning and feedback
Desktop / headless for simulation
Gamepad for manual steering
Path and accuracy reports are simulation-only; physical path tracking requires localization.

## Slide 26
CURRENT EVIDENCE
What we can demonstrate now
VIDEO TO BE ADDED
8–12 second locomotion demonstration
Temporary still: Screenshot_20261016_012632_WhatsApp.jpg
EVIDENCE BOUNDARY
Physical operation
Working Gen 2 movement
Software checks
Commands, feedback and simulation
Measurements to record
Speed, slip, power and stop latency
Document the surface and controller used; sensor streaming alone does not prove autonomous navigation.

## Slide 27
GEN 3 • DESIGN / EXPERIMENT
Gen 3 introduces alternating yaw and pitch
Gen 3 CAD — connector and joint-axis view
Reserve the actual revision from gen3-experimental-3d/cad/ and label alternating axes directly on the model.
CURRENT RESEARCH DIRECTION
Alternating joint axes
Revised connectors and plate-chain layout
Experimental 3D waveform
Dry-run scripts, CAD candidates and waveform experiments are not proof of completed 3D locomotion.

## Slide 28
NEXT EXPERIMENTS
The next experiments answer specific questions
QUESTION | OBSERVATION TO RECORD
01 How does surface contact affect forward travel and slip? | Distance and time • lateral drift • body contact
02 How repeatable are steering and stop response? | Turn response • stop delay • selected controller and surface
03 What changes when pitch joints carry the body out of the plane? | Joint clearance • contact points • voltage and current
Quantities remain blank until measured. Use the same controller and test surface for comparable records.

## Slide 29
ROADMAP
From the working planar robot to Gen 3 trials
Working Gen 2 reference
Current planar platform
→
Repeatable measurements
Contact, motion, power and stopping
→
Gen 3 assembly checks
Connectors, axes and clearance
→
Coordinated 3D trials
Experimental yaw/pitch motion
The planar platform gives us a working base for the next set of mechanical and gait experiments.
SURGE-090 • Team update • Repository URL / team names
Reference: earlier roadmap on slide 16