## Slide 1
GROUP CODE · SURGE 090
Progress Review (Design & Development)
Smart Snake Robot
with Dynamixel Smart Servo Motors
Shashank Jangir
ENTRY NO.
2024EE11048
Bhavesh Bansiwal
ENTRY NO.
2024ME10487
Mahima Chotiya
ENTRY NO.
2024ME11187
INSTITUTION
Indian Institute of Technology, Delhi
PROJECT GUIDE
Professor Amartansh Dubey
PROJECT REPOSITORY
https://github.com/shashankjangir/SurGe-090-Smart-snake-robot
Notes: Title slide for the 25% progress review of the Smart Snake Robot project, Group SURGE 090. Introduce the team and milestone scope.

## Slide 2
ACTUATOR SELECTION STUDY
Why Dynamixel Motors?
THE REQUIREMENT
A snake robot drives many joints at once. The actuator must deliver:
Precise position control
Simple wiring architecture
Scalability for multiple joints
Reliable communication
Real-time feedback
Compact size & sufficient torque
OPTIONS COMPARED
Criterion | Conventional Servo | Dynamixel Smart Servo
Communication | Individual signal wire per motor | Daisy-chain communication
Wiring Complexity | High | Low
Feedback | Not available | Position, load, temperature, voltage feedback
Controller | External controller required | Built-in controller
Scalability | Difficult for many joints | Designed for multi-joint robots
Precision | Moderate | High
Robotics Applications | Hobby projects | Research and industrial robotics

## Slide 3
ARCHITECTURE & DECISION
Daisy-Chain Architecture & Final Selection
Conventional Servo — Separate Wiring
Controller
Servo 1
Servo 2
Servo 3
Servo 4
Every motor needs its own signal wire back to the controller.
Dynamixel — Daisy-Chain
Ctrl
M1
M2
M3
M4
One cable carries power and data to every joint in sequence.
KEY LEARNINGS
Daisy-chain wiring sharply cuts cabling and assembly effort.
A controller built into every motor simplifies integration.
Real-time feedback enables future closed-loop control.
Compact form factor suits modular robot segments.
High precision and smart control fit advanced robotics.
FINAL SELECTED ACTUATOR
Dynamixel XL330 Series
Chosen for its smart serial communication, full-state feedback, compact form factor and effortless multi-joint scaling — the right fit for a multi-segment snake robot.

## Slide 4
GOALS & EXPECTED OUTCOMES
What This Project Sets Out to Build
01
Modular Architecture
A repeatable segment-based mechanical design.
02
Dynamixel Actuators
Integrate smart servos with daisy-chained control.
03
Raspberry Pi Control
A single-board-computer control system.
04
Locomotion Algorithms
Implement serpentine and gait-based motion.
05
Sensor Integration
Add sensing for future intelligent navigation.
06
Scalable Platform
Keep it maintainable and easy to extend.
Notes: Six concrete goals across mechanics, actuation, computing, control, sensing and scalability. These map to the timeline phases.

## Slide 5
WORK COMPLETED SO FAR
Quarter-One Progress Summary
OVERALL COMPLETION(till now)
25 %
Phase 1 complete · Phase 2 underway
10
Tasks done
2
Segments printed
1
Pi configured
COMPLETED TASKS
Literature review & project understanding
Hardware selection & BOM preparation
CAD design of snake-robot segment
Assembly sized to Dynamixel XL330 dims
3D printing of two prototype segments
Raspberry Pi setup & configuration
Wi-Fi connectivity testing on the Pi
Basic Raspberry Pi lab projects executed
GitHub repository created & maintained
Procurement process initiated
Notes: About a quarter done: ten tasks closed across research, mechanical design, fabrication and the compute platform.

## Slide 6
Power Supply
Raspberry Pi 5 [Central Controller]
Communication Layer (U2D2 / UART)
Dynamixel Motor Network
Robot Segments (10 × servo joints)
Control Algorithms
IMU / Force Sensors
Camera Module
Wireless Control Module
LEGEND
Implemented
In Progress
Planned Future Work
Current Implementation Status
Raspberry Pi 5 configured and tested
Communication architecture defined
Mechanical segments fabricated
Dynamixel integration pending hardware
SYSTEM ARCHITECTURE
Conceptual Block Diagram
Architecture finalized · Implementation in progress
FUTURE INTEGRATION
Notes: Controller at the centre. Solid cyan = implemented/in progress; dashed amber (sensors, camera) = designed-in but scheduled for a later phase.

## Slide 7
CAD DESIGN DEVELOPMENT
A Segment Designed Around the Motor
The CAD model is built to the exact dimensions of the Dynamixel XL330-M288 servo, using a modular, segment-based architecture focused on manufacturability and scalability.
DESIGN CONSIDERATIONS
Motor mounting — Precise seats for XL330 servo bodies.
Structural rigidity — Stiff frame to resist motion loads.
Cable routing — Clean daisy-chain channels for wiring.
Electronics ready — Space reserved for future boards.
ASSEMBLY FLOW
Motor → Segment Parts → Full Chain Assembly
① Motor
② Segment Parts
③ Full Assembly
③ Full Assembly
Notes: CAD modelled to real XL330 dimensions so printed parts mate with the actual servos. Replace the placeholder with CAD screenshots.

## Slide 8
PROTOTYPE FABRICATION
From Model to Printed Hardware
PRINTED SEGMENT — PHOTO 1
Insert photo of the first 3D-printed segment
PRINTED SEGMENT — PHOTO 2
Insert photo of the second segment / assembly
FABRICATION STATUS
Two prototype segments 3D printed
Both segments produced from the CAD model.
DONE
Initial dimensional verification done
Printed parts measured against design specs.
DONE
Physical validation of CAD initiated
Checking fit, tolerances and assembly.
NEXT
Preparing for motor-integration tests
Next: seat XL330 servos into segments.
NEXT
Notes: Two segments printed and measured, validating the CAD. Next step is servo integration. Drop prototype photos on the left.

## Slide 9
Raspberry Pi 5 received & configured
Raspberry Pi OS installation completed
Wi-Fi connectivity established
SSH & remote access explored
Basic GPIO & intro projects performed
Linux environment & Python familiarity
Raspberry Pi Platform Successfully Configured and Tested
Raspberry Pi OS Desktop
GPIO / Python Testing
SSH Remote Access
System Configuration
Development Environment Setup
PROGRESS MILESTONES
Standing Up the Compute Platform
RASPBERRY PI LEARNING & DEVELOPMENT
Notes: Control computer is live: OS installed, networked, remotely accessible, exercised with intro GPIO and Python. De-risks software before motors arrive.

## Slide 10
HARDWARE PROCUREMENT & RESOURCE AVAILABILITY
Hardware Procurement & Resource Availability
Hardware Strategy: Raspberry Pi 4 was planned in the BOM; however, a Raspberry Pi 5 was already available in the laboratory, enabling immediate software development and testing without waiting for delivery. To accelerate development, the team utilised the laboratory Raspberry Pi 5 platform while the ordered components remain under procurement.
AVAILABLE & IN USE
ORDERED — AWAITING DELIVERY
COMPLETED PREPARATORY WORK
Raspberry Pi 5 (Laboratory Resource)
Raspberry Pi Starter Kit
Raspberry Pi OS Environment
GitHub Repository
3D Printed Prototype Segments
Dynamixel XL330 Smart Servo Motors
U2D2 Communication Interface
U2D2 Power Hub Board
Dynamixel Communication Cables
5V Power Supply
ESP32 Development Board
Hardware selection finalised
Bill of Materials prepared
CAD model completed
Segment fabrication initiated
Software environment configured
DEVELOPMENT PROGRESS
✓
Component
Selection
✓
Procurement
Initiated
✓
CAD
Design
✓
Prototype
Printing
✓
RPi
Learning
⏳
Motor
Integration
Awaiting HW
→
Locomotion
Testing
Upcoming
★
Key Achievement: Although the primary Dynamixel hardware has not yet arrived, the team has successfully utilised available laboratory resources to complete design, fabrication, documentation, and software preparation activities, ensuring project progress is maintained.
Notes: Live BOM from the purchasing sheet. Compute hardware in hand; actuation and power chain ordered. Total approx Rs 33,760.

## Slide 11
REPOSITORY & DOCUMENTATION
Version Control From Day One
1
Repository created
Central home for the whole project.
2
Version control established
Tracked, reversible change history.
3
CAD files uploaded
Design source committed to the repo.
4
Design iterations documented
Every revision captured in commits.
5
Progress tracking in place
Milestones and issues logged.
6
Team collaboration workflow
Shared branches and pull requests.
GitHub repository — project root & structure
Commit history — tracked iterations & uploads
GITHUB REPOSITORY SCREENSHOTS
✓ All milestones tracked in GitHub
Notes: The repo is the single source of truth — CAD, docs, tracked iterations — with a collaboration workflow already running.

## Slide 12
PROJECT TIMELINE
Eight Phases · Currently at 25%
PHASE 1
Research & Design
Completed
1
PHASE 2
Hardware Procurement
In progress
2
PHASE 3
Mechanical Assembly
Up next
3
PHASE 4
Motor Integration
4
PHASE 5
Control Algorithms
5
PHASE 6
Sensor Integration
6
PHASE 7
Testing & Optimisation
7
PHASE 8
Final Demonstration
8
WE ARE HERE
Notes: Eight-phase plan: Phase 1 complete, Phase 2 active, Phase 3 next — about 25%. Phases 4-8 cover integration, control, sensing, testing, demo.

## Slide 13
CURRENT ACHIEVEMENTS
Concrete Wins in Quarter One
Architecture finalized
System block diagram locked.
CAD design completed
Segment modelled to motor specs.
Prototype fabrication started
Two segments printed & checked.
Pi environment established
OS, network and tooling ready.
GitHub workflow operational
Version control and docs live.
Procurement initiated
Core compute received; rest ordered.
Notes: Six headline achievements: design, fabrication, compute, tooling and procurement all moving — a working foundation.

## Slide 14
SIMULATION & VALIDATION
Simulation-Based Validation of Control Architecture
Wokwi-based simulation environment developed to validate locomotion control, sensor integration, and communication architecture before physical Dynamixel hardware arrival.
SIMULATION OBJECTIVE
A virtual testing platform to validate the control architecture before Dynamixel actuators and communication hardware arrive — enabling software development, algorithm verification, and sensor integration in parallel with procurement.
COMPONENTS SIMULATED
Controller
Sensors
Display
Actuators
ESP32 · 5-Servo joint network · MPU6050 IMU · HC-SR04 ultrasonic · SSD1306 OLED · control & communication framework
FUNCTIONAL VALIDATION COMPLETED
ENGINEERING BENEFITS
Multi-joint servo coordination
Travelling-wave serpentine gait generation
Obstacle detection via ultrasonic sensing
IMU integration for orientation feedback
OLED-based system status monitoring
Sensor–controller–actuator communication
Reduced dependence on hardware delivery timelines
Enabled early software debugging & control-architecture verification
Established migration path to Raspberry Pi 5 + Dynamixel XL330, reducing integration risk
KEY OUTCOME A complete software-validation framework was developed, allowing locomotion, sensing, and control workflows to be tested before physical robot assembly.

## Slide 15
FUTURE WORK & DEVELOPMENT ROADMAP
Planned Activities for the Next Development Phase
1
Hardware Arrival
Receive Dynamixel XL330 motors
Receive U2D2 interface
Verify purchased components
2
Mechanical Assembly
Assemble complete snake body
Install Dynamixel actuators
Route communication cables
3
Communication Setup
Configure motor IDs
Establish serial communication
Validate daisy-chain architecture
4
Locomotion Development
Port simulation code to Pi 5
Implement serpentine locomotion
Synchronize multi-joint movement
5
Sensor Integration
Integrate MPU6050 IMU
Integrate obstacle detection
Implement feedback control
6
Testing & Optimization
Motion performance testing
Power & reliability analysis
System optimization
Completed phase
Ongoing work
Future milestone
EXPECTED DELIVERABLES
Fully assembled snake robot
Dynamixel-based locomotion
Sensor-assisted navigation
Integrated Raspberry Pi 5 control system
Demonstration-ready prototype
Final SURGE project showcase
TARGET FOR NEXT REVIEW
Complete hardware integration
Demonstrate basic snake locomotion
Validate communication architecture
Validate sensing framework
Goal: ~60–70% project completion

## Slide 16
WHAT CHANGED SINCE THIS REVIEW
Generation 2 — Corrections & Cause
Slides 1–15 are unchanged from the 25% review. This slide records what has since been superseded.
Constraint
WHAT HAPPENED
2 of 10 XL330 received, then the part vanished
Six-week stall
IMPACT
Control stack written against absent hardware
Re-architecture
COMMIT a32b675 · 2026-08-20
“No dynamixel in the market. So switched to Servos”
SLIDE | THAT DECK SAID | TODAY | WHY
10 | XL330 · U2D2 · Power Hub — “ORDERED, AWAITING DELIVERY” | Order cancelled. 10× ST3215 + Waveshare ESP32 driver in hand | Part unobtainable in India
12 | “Eight Phases · Currently at 25%” | Phase 3 — Fabrication & Assembly | Eight weeks of Gen 2 work since
13 | “Prototype fabrication started” | Gen 1 segments printed; Gen 2 v6 not yet printed | Design of record changed
15 | Roadmap step 1 — “Receive Dynamixel XL330 motors” | Superseded — see slide 29 | Different motors received
WHAT IT BOUGHT 5.7× joint torque (0.52 → 2.94 N·m) · a 12 V rail · sourceable in India — consequences of the switch, not its reason. Torque budget: slide 23.
Notes: Open by saying the deck up to this point is unchanged from the 25 percent review and is being left that way deliberately - those slides are a record of what we believed then, not a claim about now. Then walk the register top to bottom. It takes about forty seconds and it pre-empts every 'but slide 10 says' interruption in the second half. Say the honest version of the pivot out loud: this was a procurement failure, not an engineering preference, and a re-architecture under a supply constraint is a legitimate result. The follow-up question a reviewer asks is 'where is your torque budget' - it is slide 23, and it did not exist at the 25 percent review.

## Slide 17
ACTUATOR RE-SELECTION
From XL330 to Waveshare ST3215
THE CONSTRAINT
The Gen 1 trade study was sound and its conclusion still holds: a snake robot needs smart serial bus servos. Only the vendor changed. XL330 became unobtainable in the Indian market after 2 of 10 units were received.
Precise absolute position control
Single-cable daisy-chain wiring
Per-joint load and current feedback
Built-in controller, no external driver per joint
Scalable to 10 coordinated joints
Procurable in India, in quantity
XL330 VS ST3215 — AS SELECTED
Criterion | Dynamixel XL330 (Gen 1) | Waveshare ST3215 (Gen 2)
Stall torque | 0.52 N·m | 2.94 N·m — 5.7× higher
Voltage rail | 5 V | 6.0–12.6 V
Stall current | 0.35 A | 2.7 A @ 12 V
Encoder | 12-bit absolute | 12-bit absolute, 0–4095
Bus protocol | Dynamixel 2.0, 1 Mbps | Feetech STS, 1 Mbps half-duplex
Driver hardware | U2D2 + Power Hub + MCU | Waveshare driver, ESP32 onboard
Availability in India | Unobtainable | In stock — 10 units held
Notes: The Gen 1 trade study is not invalidated - its conclusion was smart bus servos, and that is what we still run. Only the vendor changed, and it changed for supply reasons, not engineering ones. The torque column is the favourable consequence: 5.7x more joint torque at the same joint count. The voltage change from 5 V to 12 V is what forced the power architecture rework on slide 24.

## Slide 18
3S LiPo 1800 mAh (11.1 – 12.6 V)
Waveshare Driver + ESP32 [Robot Master]
Feetech STS Bus (1 Mbps, half-duplex)
10 × Waveshare ST3215 Servos
Robot Segments (10 × servo joints)
Gait CPG runs onboard
MPU6050 IMU (I²C 21 / 22)
ESP32 Camera (planned)
ESP-NOW → ESP32 #2 → Pi 5
LEGEND
Implemented
In Progress
Planned Future Work
Generation 2 Implementation Status
All firmware targets written and building
Servo IDs not yet assigned — all ship as ID 1
v6 segments not yet printed
ESP-NOW link not yet exercised on hardware
GEN 1 → GEN 2 ARCHITECTURE
From Tethered Pi Control to Onboard ESP32
Control moved onto the robot · Pi 5 relegated to base station · Link is now wireless
OFF-ROBOT & PLANNED
Notes: The single most important change is where control lives. In Generation 1 the Raspberry Pi was the controller and sat on the robot, tethered over USB to a U2D2. In Generation 2 the ESP32 on the Waveshare driver is the master, the Pi 5 moved off the robot entirely, and the link between them is ESP-NOW rather than a cable. That is what makes untethered operation possible. Compare this against the Generation 1 block diagram on slide 6 - the shape of the system is genuinely different, not just re-labelled.

## Slide 19
ONBOARD FIRMWARE STACK
ESP32 Firmware — Four Targets, One Bus
Firmware Strategy: the Waveshare driver's onboard ESP32 is the robot master and owns the servo bus; a second ESP32 at the base station receives telemetry over ESP-NOW and forwards it to the Pi 5 by USB serial. Bench and field firmware are mutually exclusive on the driver board — one is flashed at a time.
ROBOT ESP32 — FIELD
BASE STATION ESP32 #2
BENCH & BRING-UP TOOLS
robot_esp32 — gait CPG, 10-DOF
MPU6050 on I2C GPIO 21 / 22
Current-stall obstacle FSM
ESP-NOW telemetry transmit
base_esp32 — ESP-NOW receive
USB serial to Pi 5 @ 115200
base_station.py logs telemetry
spin_all — broadcast smoke test
assign_ids — one servo at a time
usb_servo_bridge — Python stack
PlatformIO, one env per sketch
FIRMWARE BRING-UP SEQUENCE
✓
Firmware written
✓
PlatformIO builds
✓
Broadcast smoke test
⏳
ID assignment
→
Bus verification
→
Gait on hardware
Upcoming
→
ESP-NOW telemetry
Upcoming
★
Key Achievement: all five firmware targets are written and compile clean under PlatformIO, and the broadcast smoke test drives all ten servos before any ID has been assigned — so the control stack was validated without waiting on bring-up.
Notes: Three ESP32s in total, two on the robot and one at the base. The important design point is that video and telemetry are separate radio links: ESP-NOW carries telemetry, ordinary WiFi will carry camera video. Do not try to push video through ESP-NOW - the payload cap is 250 bytes. The bring-up rail is honest: we are at ID assignment, not past it.

## Slide 20
BUS PROTOCOL
Feetech STS Control Table & Packet Format
PACKET FORMAT
All ten servos share one half-duplex TTL line at 1 Mbps. Every packet is addressed to a single ID, or to broadcast ID 0xFE, which every servo acts on and none replies to — the only safe way to drive the bus before IDs are assigned.
Header 0xFF 0xFF
ID 1–253, or 0xFE broadcast
Length parameters + 2
Instruction 0x03 = WRITE, 0x02 = READ
Parameters address, then data bytes
Checksum bitwise NOT of the byte sum
Multi-byte fields are little-endian
CONTROL TABLE — IMPLEMENTED
Register | Addr | Width and meaning
ID | 5 | 1 byte, EEPROM — factory default 1
TORQUE_ENABLE | 40 | 1 byte 0 = off, 1 = on
GOAL_POSITION | 42 | 2 bytes, little-endian, 0–4095
GOAL_SPEED | 46 | 2 bytes, steps per second
LOCK | 55 | 1 byte, EEPROM write gate
PRESENT_POSITION | 56 | 2 bytes, centre = 2048
PRESENT_CURRENT | 69 | 2 bytes, bit15 = sign, 6.5 mA/count
Notes: This is the whole interface. Two register facts matter downstream: GOAL_POSITION is little-endian and 0-4095 with centre 2048, which is a 4x scale difference from the SC-series servos the Waveshare board ships configured for; and PRESENT_CURRENT at address 69 is how we detect a stall, at 6.5 mA per count with the sign in bit 15. The 1200 mA threshold in robot_config.py is still a placeholder and needs calibrating against a real stall.

## Slide 21
CAD EVOLUTION
Segment Design v4 → v5 → v6
Design Strategy: the segment is a parametric CadQuery model, not a hand-drawn solid, so every dimension traces to a named constant and the model refuses to export if its own assumptions stop holding. v6 is the design of record; its three fixes were found by measuring the earlier versions rather than looking at them.
V4 — BASELINE
V5 — SUPERSEDED
V6 — DESIGN OF RECORD
First parametric segment
58 mm joint-to-joint pitch
Ground contact never measured
Superseded, still printable
Widened yoke rectangle
Early sidewall bug fixed
Shares v4's bounding box
Dimensional error — do not print
Belly scales now touch ground
Scales reoriented for undulation
Positive M2 motor retention
Self-check asserts all three
FABRICATION PIPELINE
✓
Parametric model
✓
Self-check passes
⏳
Probe ST3215 STEP
→
Print one segment
→
Measure friction
→
Print remaining 10
Upcoming
→
Chain assembly
Upcoming
★
Key Achievement: v6 caught three defects that v4 and v5 shared — the bottom plate sat 0.45 mm below the belly scales so 94% of ground contact was the one surface never meant to touch; the scales resisted the wrong axis for lateral undulation; and the motor had no positive retention at all.
Notes: The headline is that these defects were found by measurement, not by inspection - the model enumerates every face at minimum z and asserts which ones they are. Print v6, not v4 and definitely not v5. The friction measurement in step 5 is the real unknown: every locomotion claim in this deck assumes anisotropic belly friction that has never been measured on a printed part.

## Slide 22
STRUCTURE & LOAD PATH
v6 Load Path & Positive Motor Retention
v4 / v5 — Motor Lifts Straight Out
Horn
Slip-fit 0.4 mm
Open at top
Lightening windows
~1 mm rear wall
The motor sits in an open pocket with no fastener. Nothing resists it lifting out.
v6 — Captured in a Closed Cradle
Horn
M2
M2
M2
M2
Four M2 screws capture the motor against a closed cradle wall.
LOAD PATH
Horn face transfers joint torque to the next segment
F623ZZ flange bearing on the horn-opposite side
Bearing carries radial load off the motor shaft
14 mm bolt circle, 4 × M2 blind holes each face
Closed cradle wall reacts motor reaction torque
RETENTION — RESOLVED IN V6
Four M2 screws through a closed cradle
v4 and v5 relied on an interference fit alone. Under repeated gait loading that is a slow failure: the pocket wears, the motor rocks, and joint backlash grows. v6 adds positive fastening and restores the sidewall the lightening windows removed.
Notes: The load path point is that the motor shaft should not be carrying radial load - the F623ZZ bearing on the opposite face does that, and the horn only transfers torque. The retention fix matters more than it sounds: an interference fit that loosens turns into joint backlash, and backlash in a 10-joint chain compounds into a gait that will not track. This was found by measuring the pocket, not by looking at it.

## Slide 23
FRICTION, KEELS & TORQUE
Why v6 Can Actually Move — Friction & Torque Budget
v4 / v5 — Scales Never Touched Ground
Belly
Plate at −3.45 mm
Scales at −3.00 mm
Plate 1006 mm²
Scales 66 mm²
The plate hung 0.45 mm below the scales — 94% of ground contact was the one surface never meant to touch.
v6 — Keels Carry the Robot
Belly
Grip
Slide
Grip
Slide
Scales swept along the body: grip across it, slide along it — the asymmetry lateral undulation requires.
TORQUE BUDGET
ST3215 stall torque 2.94 N·m at 12 V
XL330 was 0.52 N·m — 5.7× less
10 joints, 58 mm pitch, ~580 mm body
Head pod adds ≈ 0.02 N·m — under 1% of budget
Torque is no longer the binding constraint
THE REMAINING UNKNOWN
Anisotropic friction ratio is unmeasured
Every locomotion claim in this deck assumes the belly grips across the body and slides along it. That ratio has never been measured on a printed part. Printing one v6 segment and measuring fore/aft versus lateral friction is the single highest-value next experiment.
Notes: Two halves. The torque half is settled - 5.7 times more joint torque than Generation 1, and the head pod barely registers against it, so torque stopped being the limiting factor the moment we switched actuators. The friction half is not settled and I want to be explicit about that. A snake robot moves by having different friction across the body than along it. v4 and v5 got that backwards and also never touched the ground with the feature that was supposed to do it. v6 fixes both in CAD, but nobody has put a printed segment on a surface and measured the ratio. Until that happens, the gait is theory.

## Slide 24
3S LiPo 1800 mAh — 20.0 Wh
Inline fuse + XT60 loop key [NOT YET HELD]
1000 µF bulk capacitor [NOT YET HELD]
Waveshare Driver VIN (6 – 12 V)
10 × ST3215 — 27 A worst-case stall
≈ 22 min at 4 A
Mean Well LRS-100-5 (5 V, 20 A)
12 V 2 A supply — ID assignment
XL6009 boost — one servo only
LEGEND
Implemented
In Progress
Planned Future Work
Power Status & Open Risks
LiPo sits inside the servo range — no conversion needed
Driver is rated 6–12 V; a full 3S pack is 12.6 V
Fuse, BMS and loop key are not yet in inventory
LiPo C-rating unverified — sets the real current ceiling
ELECTRICAL & POWER ARCHITECTURE
Field and Bench Power Paths
Robot rail resolved · No DC conversion needed · Protection hardware outstanding
BENCH PATH (TETHERED)
Notes: The resolved part is the robot rail: a 3S pack sits inside the ST3215's 6.0 to 12.6 volt window, so it feeds the driver directly with no buck or boost anywhere in the path. That removes the whole conversion problem Generation 1 had at 5 volts. Two things are not resolved and both belong on the record. First, Waveshare rates this board 6 to 12 volts, and a fully charged 3S pack is 12.6 - so we are 0.6 volts over spec at the top of every charge cycle. Second, none of the three protection parts are held yet. The 27 amp figure is worst-case all-joints-stalled, not normal draw, but it is what sizes the fuse.

## Slide 25
SAFETY ARCHITECTURE & CRITICAL GAPS
Five Protection Parts the Robot Does Not Yet Have
Inline fuse — MISSING
Nothing limits fault current on a 27 A-capable pack.
Loop-key disconnect — MISSING
No safe way to isolate the battery from the bus.
LiPo alarm / BMS — MISSING
No cell-level undervoltage protection below 3.0 V.
Bulk capacitor — MISSING
Servo inrush transients reach the driver unsuppressed.
Balance charger & bag — MISSING
No safe charge, balance or storage path for the pack.
Current-stall limit — IN FIRMWARE
Software torque cap works, but is not a fuse.
Notes: This is the slide I would rather not need. Five of the six cards are amber and they are all cheap - roughly 3600 rupees for the whole row. The reason it is on the deck rather than buried in a spreadsheet is that a 3S lithium polymer pack capable of 27 amps, with no fuse, no cell monitoring and no disconnect, is the one genuinely hazardous thing in this project. The sixth card is deliberate: the firmware current limit is real and it works, but software cannot protect against a short circuit. Nothing goes on the LiPo until the first three are fitted.

## Slide 26
GAIT & OBSTACLE RESPONSE
Gait Generation and the Evasion State Machine
Lateral Undulation — Travelling Wave
CPG
Joint 1 φ = 0°
Joint 2 φ = 72°
Joint 3 φ = 144°
Joint 4 φ = 216°
A serpenoid phase offset propagates down the chain at 50 Hz; amplitude 400 ticks ≈ 35°.
Evasion Finite State Machine
FSM
RUN
STALL
BACK
TURN
A sustained current rise trips STALL; the robot reverses, turns away, then resumes.
GAIT PARAMETERS
Control loop 50 Hz
Amplitude 400 encoder ticks ≈ 35°
Phase offset 72° per joint, 10 joints
Goal position written as a sync payload
Gait continues if the IMU is absent
OBSTACLE DETECTION
Proprioceptive — no external sensor
Collision is inferred from PRESENT_CURRENT at address 69 rather than a rangefinder. The threshold is still a placeholder at 1200 mA and must be calibrated against a measured free-run and stall current before it can be trusted.
Notes: The gait is a central pattern generator - a travelling sine wave with a fixed phase offset per joint, which is the standard lateral undulation formulation. The part worth drawing attention to is obstacle detection: there is no ultrasonic sensor and no rangefinder in the loop. The robot notices an obstacle because a joint draws more current than it should, which is proprioception rather than exteroception. That is elegant and it costs nothing in hardware, but the threshold is a guess until we measure a real stall on a real segment.

## Slide 27
VERIFICATION & MOCK-MODE RESULTS
What Has Been Proven Without Hardware
v6 CAD self-check
Model refuses to export if its assumptions break.
Mock mode — SURGE_MOCK=1
Full gait stack runs with no servos attached.
Wokwi simulation
ESP32, servos, IMU and display validated virtually.
PlatformIO — five targets
All firmware environments compile clean.
Broadcast smoke test
Ten servos driven before any ID was assigned.
Hardware verification
Ping, stall calibration and gait still outstanding.
Notes: The honest framing is that this is verification without hardware, which is worth a lot but is not the same as a working robot. The five green cards are real: the CAD model asserts its own ground-contact geometry, the Python stack runs a full gait in mock mode, the simulation covers the electronics, every firmware target builds, and the broadcast test moved all ten servos on the bench. The amber card is the point of the slide - nothing has been calibrated against a real stall current yet, and that is the next measurement.

## Slide 28
INVENTORY, BUDGET & PROCUREMENT GAPS
What We Hold, What We Still Need
Budget Position: Gen 1 spend was approximately ₹33,760 of the ₹1,00,000 SURGE grant. Remaining procurement is estimated at ₹10,200 and is almost entirely consumables and safety hardware — the expensive actuator and compute line items are already held.
IN HAND — 9 LINE ITEMS
MISSING — CRITICAL (SAFETY)
MISSING — HIGH PRIORITY
10× Waveshare ST3215 servos
Waveshare driver with ESP32
ESP32 #2, Pi 5 8 GB, MPU6050
3S LiPo 1800 mAh, Mean Well 5 V
Camera Module 3, XL6009 boost
Inline fuse and holder
LiPo alarm / BMS module
XT60 loop-key disconnect
Without these the pack is unsafe
3S balance charger, storage bag
Servo daisy-chain cables ×12
F623ZZ bearings, M2 fasteners
PLA+ filament, TPU belly pads
PROCUREMENT STATUS
✓
Actuators received
✓
Compute received
✓
Power source held
⏳
Safety parts
→
Fasteners & bearings
→
Filament & pads
Upcoming
→
Camera for ESP32
Upcoming
★
Key Achievement: the actuator blocker that stalled Generation 1 is cleared — all ten servos, the driver board and the power source are in hand. Every remaining gap is a low-cost consumable, not a supply-chain risk.
Notes: Be direct about the sunk Gen 1 cost. The favourable point is that Gen 2 needs only consumables and safety parts and the grant covers it comfortably. The critical row is not optional - running a 3S LiPo with no fuse, no BMS and no disconnect is the one genuinely unsafe thing in this project. Verify the ST3215 purchase cost before presenting; the inventory lists them as held but records no price.

## Slide 29
ROADMAP
Path to Demonstration — Generation 2
PHASE 1
Power Verification
In progress
1
PHASE 2
Servo Bring-Up
Up next
2
PHASE 3
Segment Fabrication
Planned
3
PHASE 4
Mechanical Assembly
4
PHASE 5
Field Integration
5
PHASE 6
Locomotion Trials
6
PHASE 7
Characterisation
7
PHASE 8
Final Demonstration
8
WE ARE HERE
Replaces the Generation 1 roadmap on slide 15, which was written around Dynamixel XL330 delivery and is now obsolete.
Notes: Open by naming slide 15 and saying plainly that it is superseded - do not let the audience find two roadmaps on their own and wonder which one is live. The eight phases here are the actual next steps from the hardware inventory, not a re-skin of the old plan. Phase 1 is where we are: the pack cannot go on the robot until the fuse, loop key and BMS are fitted. Close on phase 3, because it contains the one experiment everything else depends on - printing a v6 segment and measuring whether the belly friction is actually anisotropic. If it is not, the gait does not work and we would rather know that before printing ten more segments. Target for the next review is first translating locomotion on hardware, which is a milestone you can watch rather than a percentage you have to trust.